Copyright 2012 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 079219 - ACOUSTICAL JOINT SEALANTS

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on Masterworks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on Masterworks/Supporting Information.

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section includes acoustical joint sealants.

ACTION SUBMITTALS

Product Data: For each acoustical joint sealant.

LEED Submittals:

"Product Data for Credit IEQ 4.1" Subparagraph below applies to LEED-NC, LEED-CI, and LEED-CS; coordinate with requirements for sealants and sealant primers.

Product Data for Credit IEQ 4.1: For sealants and sealant primers used inside the weatherproofing system, documentation including printed statement of VOC content.

"Laboratory Test Reports for Credit IEQ 4" Subparagraph below applies to LEED for Schools.

Laboratory Test Reports for Credit IEQ 4: For sealants and sealant primers used inside the weatherproofing system, documentation indicating that products comply with the testing and product requirements of the California Department of Public Health's (formerly, the California Department of Health Services') "Standard Method for the Testing and Evaluation of Volatile Organic Chemical Emissions from Indoor Sources Using Environmental Chambers."

Samples: For each kind and color of acoustical joint sealant required.

Acoustical-Joint-Sealant Schedule: Include the following information:

Joint-sealant application, joint location, and designation.

Joint-sealant manufacturer and product name.

Joint-sealant formulation.

Joint-sealant color.

INFORMATIONAL SUBMITTALS

Product test reports.

Sample warranties.

WARRANTY

When warranties are required, verify with Owner's counsel that special warranties stated in this article are not less than remedies available to Owner under prevailing local laws.

Special Installer's Warranty: Installer agrees to repair or replace acoustical joint sealants that do not comply with performance and other requirements specified in this Section within specified warranty period.

Verify available warranties and warranty periods for acoustical joint-sealant installation.

Warranty Period: [Two] <Insert number> years from date of Substantial Completion.

Special Manufacturer's Warranty: Manufacturer agrees to furnish acoustical joint sealants to repair or replace those joint sealants that do not comply with performance and other requirements specified in this Section within specified warranty period.

Verify available warranties and warranty periods for acoustical joint sealants.

Warranty Period: <Insert number> years from date of Substantial Completion.

PRODUCTS

See Editing Instruction No. 1 in the Evaluations for cautions about named manufacturers and products. For an explanation of options and Contractor's product selection procedures, see Section 016000 "Product Requirements."

PERFORMANCE REQUIREMENTS

Provide acoustical joint-sealant products that effectively reduce airborne sound transmission through perimeter joints and openings in building construction, as demonstrated by testing representative assemblies according to ASTM E 90.

VOC Content of Interior Sealants: Sealants and sealant primers shall comply with the following:

Retain subparagraph below if required for LEED-NC, LEED-CI, or LEED-CS Credit IEQ 4.1.

Acoustical sealants and sealant primers shall have a VOC content of [250] <Insert value> g/L or less.

Retain "Low-Emitting Interior Sealants" Paragraph below if required for LEED for Schools Credit IEQ 4.1.

Low-Emitting Interior Sealants: Acoustical sealants and sealant primers shall comply with the testing and product requirements of the California Department of Public Health's (formerly, the California Department of Health Services') "Standard Method for the Testing and Evaluation of Volatile Organic Chemical Emissions from Indoor Sources Using Environmental Chambers."

ACOUSTICAL JOINT SEALANTS

Acoustical Sealant: Manufacturer's standard nonsag, paintable, nonstaining latex acoustical sealant complying with ASTM C 834.

<Double click here to find, evaluate, and insert list of manufacturers and products.>

Colors of Exposed Acoustical Joint Sealants: [As indicated by manufacturer's designations] [Match Architect's samples] [As selected by Architect from manufacturer's full range of colors] <Insert color>.

Retain "Primer" Paragraph below if joint priming is required.

Primer: Material recommended by acoustical-joint-sealant manufacturer where required for adhesion of sealant to joint substrates.

Cleaners for Nonporous Surfaces: Chemical cleaners acceptable to manufacturers of sealants and sealant backing materials.

Masking Tape: Nonstaining, nonabsorbent material compatible with joint sealants and surfaces adjacent to joints.

EXECUTION

PREPARATION

Surface Cleaning of Joints: Clean out joints immediately before installing acoustical joint sealants to comply with joint-sealant manufacturer's written instructions.

Joint Priming: Prime joint substrates where recommended by acoustical-joint-sealant manufacturer.

Masking Tape: Use masking tape where required to prevent contact of sealant or primer with adjoining surfaces.

INSTALLATION OF ACOUSTICAL JOINT SEALANTS

Comply with acoustical joint-sealant manufacturer's written installation instructions unless more stringent requirements apply.

Retain "STC-Rated Assemblies" and "Acoustical Ceiling Areas" Paragraphs below as required, or revise to include additional applications to suit Project.

STC-Rated Assemblies: Seal construction at perimeters, behind control joints, and at openings and penetrations with a continuous bead of acoustical joint sealant. Install acoustical joint sealants at both faces of partitions, at perimeters, and through penetrations. Comply with ASTM C 919, ASTM C 1193, and manufacturer's written recommendations for closing off sound-flanking paths around or through assemblies, including sealing partitions to underside of floor slabs above acoustical ceilings.

Acoustical Ceiling Areas: Apply acoustical joint sealant at perimeter edge moldings of acoustical ceiling areas in a continuous ribbon concealed on back of vertical legs of moldings before they are installed.

END OF SECTION 079219