Copyright 2014 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 092900 - GYPSUM BOARD

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section Includes:

Interior gypsum board.

Exterior gypsum board for ceilings and soffits.

Tile backing panels in first subparagraph below may be specified in this Section or in Section 093013 "Ceramic Tiling."

Tile backing panels.

ACTION SUBMITTALS

Product Data: For each type of product.

Samples: For each texture finish indicated on same backing indicated for Work.

DELIVERY, STORAGE and HANDLING

Deliver materials in original packages, containers or bundles bearing brand name and identification of manufacturer or supplier.

Store materials inside under cover and keep them dry and protected against damage from weather, direct sunlight, surface contamination, corrosion, construction traffic and other causes. Neatly stack gypsum boards flat to prevent sagging.  Gypsum boards shall not be stored in direct contact with concrete slabs.

Handle gypsum boards to prevent damage to edges, ends, and surfaces. Do not bend or otherwise damage metal corner beads and trim.

PROJECT CONDITIONS

Environmental Limitations: Comply with ASTM C 840 requirements or gypsum board manufacturer's written recommendations, whichever are more stringent.

Do not install interior products until installation areas are enclosed and conditioned.

Do not install panels that are wet, those that are moisture damaged, and those that are mold damaged.

PRODUCTS

Manufacturers and products listed in SpecAgent and Masterworks Paragraph Builder are neither recommended nor endorsed by the AIA or ARCOM. Before inserting names, verify that manufacturers and products listed there comply with requirements retained or revised in descriptions and are both available and suitable for the intended applications. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

PERFORMANCE REQUIREMENTS

Retain "Fire-Resistance-Rated Assemblies" Paragraph below where gypsum board is part of fire-resistance-rated assemblies. Indicate design designations of specific assemblies on Drawings.

Fire-Resistance-Rated Assemblies: For fire-resistance-rated assemblies, provide materials and construction identical to those tested in assembly indicated according to ASTM E 119 by an independent testing agency.

Retain "STC-Rated Assemblies" Paragraph below where gypsum board is part of STC-rated assemblies. Indicate design designations of specific assemblies on Drawings.

STC-Rated Assemblies: For STC-rated assemblies, provide materials and construction identical to those tested in assembly indicated according to ASTM E 90 and classified according to ASTM E 413 by an independent testing agency.

GYPSUM BOARD, GENERAL

Size: Provide maximum lengths and widths available that will minimize joints in each area and that correspond with support system indicated.

INTERIOR GYPSUM BOARD

General.  Gypsum board panels complying with ASTM C 1396/C 1396M, as applicable to type of gypsum board indicated and whichever is more stringent.

Available Manufacturers: Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

American Gypsum.

CertainTeed Corporation.

Georgia-Pacific Building Products.

National Gypsum Company.

USG Corporation.

Consider deleting paragraph below and only retaining type X in instances where both type X and regular gypsum board panels are used.

Gypsum Wallboard: ASTM C 1396/C 1396M.

5/8” thick gypsum board panels are minimum for walls and ceilings, adjust as necessary to meet requirements.

Gypsum wallboard is also available in 1/4- and 3/8-inch (6.4- and 9.5-mm) thicknesses for limited applications.

Thickness: 5/8 inch (15.9 mm).

Long Edges:  Tapered.

Gypsum Board, Type X: ASTM C 1396/C 1396M.

Thickness: 5/8 inch (15.9 mm).

Long Edges:  Tapered.

Flexible Gypsum Board: ASTM C 1396/C 1396M. Manufactured to bend to fit radii and to be more flexible than standard regular-type gypsum board of same thickness.

Thickness: 1/4 inch (6.4 mm).

Long Edges: Tapered.

Gypsum Ceiling Board: ASTM C 1396/C 1396M.

Thickness: 1/2 inch (12.7 mm).

Long Edges: Tapered.

The foil backing on gypsum board in "Foil-Backed Gypsum Board" Paragraph below creates a vapor barrier. Verify limitations and proper uses with manufacturers.

Foil-Backed Gypsum Board: ASTM C 1396/C 1396M.

Core: [As indicated on Drawings] [3/8 inch (9.5 mm), regular type] [1/2 inch (12.7 mm), regular type] [5/8 inch (15.9 mm), Type X] [Type C as required by fire-resistance-rated assembly indicated on Drawings].

Long Edges:  Tapered.

"Abuse-Resistant Gypsum Board" Paragraph below describes products tested according to ASTM C 1629/C 1629M for resistance to abrasion, indentation, and soft-body impact.

"Impact-Resistant Gypsum Board" Paragraph below describes products tested according to ASTM C 1629/C 1629M for resistance to abrasion, indentation, and soft- and hard-body impact.

See "Abuse- and Impact-Resistant Gypsum Board" Article in the Evaluations for additional information. Verify availability with manufacturers.

Abuse Resistant: ASTM C 1629/C 1629M.

Abrasion-Resistant Gypsum Board

Core:  As indicated on Drawings 5/8 inch (15.9 mm), Type X.

Surface Abrasion: Meets or exceeds [Level 2] [Level 3] requirements.

Surface Indentation: Meets or exceeds [Level 1] [Level 2] requirements.

Single-Drop Soft-Body Impact: Meets or exceeds [Level 1] [Level 2] [Level 3] requirements.

Long Edges: Tapered.

Mold Resistance: ASTM D 3273, score of 10 as rated according to ASTM D 3274.

"Impact-Resistant Gypsum Board" Paragraph below describes products tested according to ASTM C 1629/C 1629M for resistance to abrasion, indentation, and soft- and hard-body impact. See "Abuse- and Impact-Resistant Gypsum Board" Article in the Evaluations for additional information. Verify availability with manufacturers.

Impact-Resistant Gypsum Board

Core:  5/8 inch (15.9 mm), Type X.

Surface Abrasion: Meets or exceeds [Level 2] [Level 3] requirements.

Surface Indentation: Meets or exceeds [Level 1] [Level 2] requirements.

Single-Drop Soft-Body Impact: Meets or exceeds [Level 1] [Level 2] [Level 3] requirements.

Hard-Body Impact: Meets or exceeds [Level 1] [Level 2] [Level 3] requirements according to test in Annex A1.

Long Edges: Tapered.

Mold Resistance: ASTM D 3273, score of 10 as rated according to ASTM D 3274.

Mold-Resistant Gypsum Board: ASTM C 1396/C 1396M. With moisture- and mold-resistant core and paper surfaces.

Core: [As indicated] [1/2 inch (12.7 mm), regular type] [5/8 inch (15.9 mm), Type X].

Long Edges: Tapered.

Mold Resistance: ASTM D 3273, score of 10 as rated according to ASTM D 3274.

SPECIALTY GYPSUM BOARD

Type C gypsum board has fire-resistive capability greater than that of Type X. Design designations of independent testing agencies indicated on Drawings generally determine product requirements for Type C gypsum board. Type C gypsum board from different manufacturers cannot be intermixed because the ratings apply only to assemblies identical in materials and construction to those tested.

Gypsum Board, Type C: ASTM C 1396/C 1396M. Manufactured to have increased fire-resistive capability.

Available Manufacturers: Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

American Gypsum.

CertainTeed Corporation.

Georgia-Pacific Building Products.

National Gypsum Company.

USG Corporation.

Type C gypsum board is available in 1/2- and 5/8-inch (12.7- and 15.9-mm) thicknesses.

Thickness: As required by fire-resistance-rated assembly indicated on Drawings.

Long Edges: Tapered.

EXTERIOR GYPSUM BOARD FOR CEILINGS AND SOFFITS

Exterior Gypsum Soffit Board: ASTM C 1396/C 1396M, with manufacturer's standard edges.

Available Manufacturers: Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

American Gypsum.

CertainTeed Corporation.

Georgia-Pacific Building Products.

National Gypsum Company.

USG Corporation.

Core: [As indicated] [1/2 inch (12.7 mm), regular type] [5/8 inch (15.9 mm), Type X].

Glass-Mat Gypsum Sheathing Board: ASTM C 1177/C 1177M, with fiberglass mat laminated to both sides and with manufacturer's standard edges.

<Double click here to find, evaluate, and insert list of manufacturers and products.>

Core: [As indicated] [1/2 inch (12.7 mm), regular type] [5/8 inch (15.9 mm), Type X].

TILE BACKING PANELS

Preference is for Tile backing panels to be specified in this Section, it can be acceptable to specify in Section 093013 "Ceramic Tiling.", as long as the criteria contained in this section are duplicated.

Cementitious Backer Units: ANSI A118.9 and ASTM C 1288 or ASTM C 1325, with manufacturer's standard edges.

Available Manufacturers: Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

CertainTeed Corporation.

Custom Building Products.

National Gypsum Company.

USG Corporation.

Thickness:  [1/2 inch (12.7 mm)] [5/8 inch (15.9 mm)] [As indicated].

Mold Resistance: ASTM D 3273, score of 10 as rated according to ASTM D 3274.

TRIM ACCESSORIES

Interior Trim: ASTM C 1047.

Material:  Galvanized or aluminum-coated steel sheet or rolled zinc.

Shapes:

Cornerbead.

Bullnose bead.

LC-Bead: J-shaped; exposed long flange receives joint compound.

L-Bead: L-shaped; exposed long flange receives joint compound.

U-Bead: J-shaped; exposed short flange does not receive joint compound.

Expansion (control) joint.

Curved-Edge Cornerbead: With notched or flexible flanges.

Exterior Trim: ASTM C 1047.

Material: [Hot-dip galvanized-steel sheet, plastic, or rolled zinc] <Insert material>.

Shapes:

Cornerbead.

LC-Bead: J-shaped; exposed long flange receives joint compound.

Expansion (Control) Joint: One-piece, rolled zinc with V-shaped slot and removable strip covering slot opening.

JOINT TREATMENT AND FINISH MATERIALS

General: Comply with ASTM C 475/C 475M.

Joint Tape:

Interior Gypsum Board: Paper.

Exterior Gypsum Soffit Board: Paper.

Glass-Mat Gypsum Sheathing Board: 10-by-10 glass mesh.

Tile Backing Panels: As recommended by panel manufacturer.

Joint Compound for Interior Gypsum Board: For each coat, use formulation that is compatible with other compounds applied on previous or for successive coats.

Prefilling: At open joints, rounded or beveled panel edges, and damaged surface areas, use setting-type taping compound.

Embedding and First Coat: For embedding tape and first coat on joints, fasteners, and trim flanges, use setting-type taping compound.

Fill Coat: For second coat, use setting-type, sandable topping compound.

Finish Coat: For third coat, use setting-type, sandable topping compound.

Skim Coat: For final coat of Level 5 finish, use [setting-type, sandable topping compound] [drying-type, all-purpose compound] [high-build interior coating product designed for application by airless sprayer and to be used instead of skim coat to produce Level 5 finish].

Joint Compound for Exterior Applications:

Exterior Gypsum Soffit Board: Use setting-type taping compound and setting-type, sandable topping compound.

Glass-Mat Gypsum Sheathing Board: As recommended by sheathing board manufacturer.

Joint Compound for Tile Backing Panels:

Cementitious Backer Units: As recommended by backer unit manufacturer.

AUXILIARY MATERIALS

General: Provide auxiliary materials that comply with referenced installation standards and manufacturer's written instructions.

Steel Drill Screws: ASTM C 1002 unless otherwise indicated.

Retain first subparagraph below if panels are attached to cold-formed metal framing specified in Section 054000 "Cold-Formed Metal Framing."

Use screws complying with ASTM C 954 for fastening panels to steel members from 0.033 to 0.112 inch (0.84 to 2.84 mm) thick.

For fastening cementitious backer units, use screws of type and size recommended by panel manufacturer.

Sound-Attenuation Blankets: ASTM C 665, Type I (blankets without membrane facing) produced by combining thermosetting resins with mineral fibers manufactured from glass, slag wool, or rock wool.

Fire-Resistance-Rated Assemblies: Comply with mineral-fiber requirements of assembly.

Acoustical Joint Sealant: Manufacturer's standard nonsag, paintable, nonstaining latex sealant complying with ASTM C 834. Product effectively reduces airborne sound transmission through perimeter joints and openings in building construction as demonstrated by testing representative assemblies according to ASTM E 90.

Available Manufacturers: Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Hilti, Inc.

Pecora Corporation.

Specified Technologies, Inc.

USG Corporation.

Acoustical joint sealant shall have a VOC content of [250] <Insert value> g/L or less.

Thermal Insulation: As specified in Section 072100 "Thermal Insulation."

EXECUTION

EXAMINATION

Examine areas and substrates, with Installer present, and including welded hollow-metal frames and framing, for compliance with requirements and other conditions affecting performance.

Examine panels before installation. Reject panels that are wet, moisture damaged, and mold damaged.

Proceed with installation only after unsatisfactory conditions have been corrected.

APPLYING AND FINISHING PANELS, GENERAL

Comply with ASTM C 840.

Install sound attenuation blankets before installing gypsum panels, unless blankets are readily installed after panels have been installed on one side.

Install ceiling/soffit panels across framing to minimize the number of abutting end joints and to avoid abutting end joints in central area of each ceiling. Stagger abutting end joints of adjacent panels not less than one framing member.

Install panels with face side out. Butt panels together for a light contact at edges and ends with not more than 1/16 inch of open space between panels. Do not force into place.

E. Locate edge and end joints over supports, except in ceiling applications where intermediate supports or gypsum board back-blocking is provided behind end joints. Do not place tapered edges against cut edges or ends. Stagger vertical joints on opposite sides of partitions. Do not make joints other than control joints at corners of framed openings.

Form control and expansion joints with space between edges of adjoining gypsum panels.

Cover both faces of support framing with gypsum panels in concealed spaces (above ceilings, etc.), except in chases braced internally.

Unless concealed application is indicated or required for sound, fire, air, or smoke ratings, coverage may be accomplished with scraps of not less than 8 sq. ft. in area.

Fit gypsum panels around ducts, pipes, and conduits.

Where partitions intersect structural members projecting below underside of floor/roof slabs and decks, cut gypsum panels to fit profile formed by structural members; allow 1/4- to 3/8-inch- wide joints to install sealant.

Attach gypsum panels to framing provided at openings and cutouts.

Indicate perimeter isolation on Drawings. See "Crack Control" Article in the Evaluations.

Isolate perimeter of gypsum board applied to non-load-bearing partitions at structural abutments. Provide 1/4- to 1/2-inch- (6.4- to 12.7-mm-) wide spaces at these locations and trim edges with edge trim where edges of panels are exposed. Seal joints between edges and abutting structural surfaces with acoustical sealant.

Attachment to Steel Framing: Attach panels so leading edge or end of each panel is attached to open (unsupported) edges of stud flanges first.

Wood Framing: Install gypsum panels over wood framing, with floating internal corner construction. Do not attach gypsum panels across the flat grain of wide-dimension lumber, including floor joists and headers. Float gypsum panels over these members, or provide control joints to counteract wood shrinkage.

STC-Rated Assemblies: Seal construction at perimeters, behind control joints, and at openings and penetrations with a continuous bead of acoustical sealant. Install acoustical sealant at both faces of partitions at perimeters and through penetrations. Comply with ASTM C 919 and with manufacturer's written recommendations for locating edge trim and closing off sound-flanking paths around or through assemblies, including sealing partitions above acoustical ceilings.

Space fasteners in gypsum panels according to referenced gypsum board application and finishing standard and manufacturer's written recommendations.

Space fasteners in panels that are tile substrates a maximum of 8 inches o.c., unless otherwise recommended by manufacturer or referenced standards.

APPLYING INTERIOR GYPSUM BOARD

Single-Layer Application:

On ceilings, apply gypsum panels before wall/partition board application to greatest extent possible and at right angles to framing, unless otherwise indicated.

On partitions/walls, apply gypsum panels vertically (parallel to framing), unless otherwise indicated or required by fire-resistance-rated assembly, and minimize end joints.

Stagger abutting end joints not less than one framing member in alternate courses of panels.

At stairwells and other high walls, install panels horizontally, unless otherwise indicated or required by fire-resistance-rated assembly.

On Z-furring members, apply gypsum panels vertically (parallel to framing) with no end joints. Locate edge joints over furring members.

Fastening Methods: Apply gypsum panels to supports with steel drill screws.

Multilayer Application:

On ceilings, apply gypsum board indicated for base layers before applying base layers on walls/partitions; apply face layers in same sequence. Apply base layers at right angles to framing members and offset face-layer joints 1 framing member, 16 inches minimum from parallel base-layer joints, unless otherwise indicated or required by fire-resistance-rated assembly.

On partitions/walls, apply gypsum board indicated for base layers and face layers vertically (parallel to framing) with joints of base layers located over stud or furring member and face-layer joints offset at least one stud or furring member with base-layer joints, unless otherwise indicated or required by fire-resistance-rated assembly. Stagger joints on opposite sides of partitions.

On Z-furring members, apply base layer vertically (parallel to framing) and face layer either vertically (parallel to framing) or horizontally (perpendicular to framing) with vertical joints offset at least one furring member. Locate edge joints of base layer over furring members.

Fastening Methods: Fasten base layers and face layers separately to supports with screws.

APPLYING TILE BACKING PANELS

Cementitious Backer Units: Comply with manufacturer's written installation instructions and install at locations indicated to receive tile. Install with 1/4-inch gap where panels abut other construction or penetrations.

Where tile backing panels abut other types of panels in same plane, shim surfaces to produce a uniform plane across panel surfaces.

INSTALLING TRIM ACCESSORIES

For trim with back flanges intended for fasteners, attach to framing with same fasteners used for panels. Otherwise, attach trim according to manufacturer's written instructions.

Control Joints: Install control joints according to ASTM C 840 at locations indicated on Drawings and as follows:

Install where a partition, wall, or ceiling traverses a construction joint (expansion, seismic or building control element) in the base building structure.

Install where movement may occur at joints in a wall or partition supported by building systems that move differentially.

Install where a wall or partition runs in an uninterrupted straight plane exceeding 30 linear ft .

Install in interior ceilings with perimeter relief so that linear dimensions between control joints do not exceed 50 ft and total area between control joints does not exceed 2,500 sq ft.

Install in interior ceilings without perimeter relief so that linear dimensions between control joints do not exceed 30 ft and total area between control joints does not exceed 900 sq ft .

Install in exterior ceilings and soffits so that linear dimensions between control joints do not exceed 30 ft and total area between control joints does not exceed 900 sq ft .

Install where ceiling framing members change direction.

Install at one side of door frames. Full height door frames shall be considered equivalent to a control joint.

Install all control joints at specific locations approved by the Architect for visual effect and as indicated in the drawings.

Interior Trim: Install in the following locations:

Cornerbead: Use at outside corners, unless otherwise indicated.

L-Bead: Use where indicated.

U-Bead: Use at exposed panel edges.

FINISHING GYPSUM BOARD

General: Treat gypsum board joints, interior angles, edge trim, control joints, penetrations, fastener heads, surface defects, and elsewhere as required to prepare gypsum board surfaces for decoration. Promptly remove residual joint compound from adjacent surfaces.

Prefill open joints[, rounded or beveled edges,] and damaged surface areas.

Apply joint tape over gypsum board joints, except for trim products specifically indicated as not intended to receive tape.

See "Gypsum Board Finish Levels" Article in the Evaluations for a discussion of requirements of various levels.

Gypsum Board Finish Levels: Finish panels to levels indicated below and according to ASTM C 840:

Level 1: Ceiling plenum areas, concealed areas, and where indicated.

Level 2:  [Where indicated on Drawings] <Insert locations>.

Level 3: [Where indicated on Drawings] <Insert locations>.

Level 4: [At panel surfaces that will be exposed to view unless otherwise indicated] <Insert locations>.

Primer and its application to surfaces are specified in Section 099123 "Interior Painting."

Level 5: [Where indicated on Drawings] <Insert locations>.

Primer and its application to surfaces are specified in Section 099123 "Interior Painting."

Glass-Mat Gypsum Sheathing Board: Finish according to manufacturer's written instructions for use as exposed soffit board.

Cementitious Backer Units: Finish according to manufacturer's written instructions.

FIELD QUALITY CONTROL

This paragraph contains important information regarding above ceiling inspections and has implications on schedule and architect’s responsibilities.  In most instances, this should be retained and part of the field report.

Above-Ceiling Observation: Before Contractor installs gypsum board ceilings, Architect will conduct an above-ceiling observation and report deficiencies in the Work observed. Do not proceed with installation of gypsum board to ceiling support framing until deficiencies have been corrected.

Notify Owner and Architect seven days in advance of date and time when Project, or part of Project, will be ready for above-ceiling observation.

Consider the options below carefully and edit to suit the Project accordingly.

Before notifying Architect, complete the following in areas to receive gypsum board ceilings:

Installation of 80 percent of lighting fixtures, powered for operation.

Installation, insulation, and leak and pressure testing of water piping systems.

Installation of air-duct systems.

Installation of air devices.

Installation of mechanical system control-air tubing.

Installation of ceiling support framing.

PROTECTION

Protect installed products from damage from weather, condensation, direct sunlight, construction, and other causes during remainder of the construction period.

Remove and replace panels that are wet, moisture damaged, and mold damaged.

END OF SECTION 092900